TREE PRESERVATION PLAN

Site Plan Review                                        City of Saint Paul

WHAT IS A TREE PRESERVATION PLAN?

A Tree Preservation Plan is a site plan that shows:

-	The existing trees on the site

-	Existing and proposed grading

-	New development on the site (such as buildings, paving, changes to existing grades)

-	Measures that will be taken to protect the existing trees

-	Any new trees that will be planted on the site

WHEN IS A TREE PRESERVATION PLAN REQUIRED?

A Tree Preservation Plan is required for any development:

-	Anywhere in the City if it affects slopes steeper than 12%

-	In the City’s Tree Preservation District (located south of Lower Afton Road in Highwood)

For these developments, a Tree Preservation Plan must be submitted before the City will approve any application for:

-	Site plan review,  grading permit, lot split or plat (This requirement is waived if the applicant can demonstrate that there are no existing trees within the limits of the area that will be disturbed by construction)

-	A building permit that requires the removal of a tree 12 inches in diameter or larger.

No grading, tree removal or other site preparation can occur until a Tree Preservation Plan has been approved.

WHAT NEEDS TO  BE SHOWN ON THE TREE PRESERVATION PLAN?

The Plan must show the limits of the area that will be affected by any construction or grading.  Within those limits the following information must be shown:

-	Buildings     The location of all proposed buildings, driveways and other paving, decks etc.

-	Grading   Existing and proposed grading must be indicated by 2 foot contours

-	Existing trees   All existing trees larger than 6 inches in diameter within the construction/grading limits of the development must be shown on the plan and identified by species.  The drip line of these trees must be shown.  The Plan must show which existing trees will be saved and which trees will be removed.

-	Tree protection measures     The Plan must show what will be done to protect existing trees during construction.  One common measure is installing construction fence around the trees that will be saved.  This fence should be installed at the drip line of the tree or as close to the drip line as possible.  A detail of this is shown on back of this handout and should be added to the Plan.

-	Replacement trees      If trees are removed, the property owner may be required to plant new trees.  The Plan must show the location of these trees. These trees must be identified by species and size.  Minimum size is 2.5 inch diameter.  Staff can advise you on the species to plant.

WHO CAN PREPARE A TREE PRESERVATION PLAN?

The Plan must be prepared by a registered landscape architect, forester or land surveyor.

SUBMITTAL REQUIREMENTS

For any project that requires a Tree Preservation Plan, the following must be submitted to the City of Saint Paul’s Department of Safety and Inspections (DSI) at 8 East 4th Street #200, Saint Paul, MN 55101

-	Application Form       An "Application for Site Plan Review" must be filled out.

-	Application Fee        For projects that require Site Plan Review, the standard fee for Site Plan Review includes the cost of reviewing the Tree Preservation Plan.  For all other projects, the fee for reviewing the Tree Preservation Plan is $110.  (Site Plan Review is required except for one and two family homes on relatively flat sites.) Checks should be made payable to the "City of Saint Paul".

-	Tree Preservation Plan      Five copies of the Tree Preservation Plan must be submitted with the application.  The Plan must be drawn to scale (such as 1" = 20') and folded to 8-1/2 x 11 size.

PRESERVING EXISTING TREES

-	Site planning to avoid trees     An inventory of existing trees must be done.  The house, driveway, decks, etc. should be located to avoid large trees as much as possible.  Grading should minimize cut and fill over tree roots.

-	Protecting trees during construction:   Trees that will be preserved must be protected from damage during construction.  The most common method is installing construction fence around the trees that will be saved. Construction fence should be installed at the drip line of the tree or as close to the drip line as possible.  A detail showing how to install this fence is shown on this handout and must be added to the Plan.

PLANTING REPLACEMENT TREES

While development should save as many trees as possible, it is recognized that some trees may have to be removed.  Trees removed for development or reasonably anticipated to be lost due to development must be replaced according to the following requirements:

-	Individual trees of at least 12 inches in diameter but less than 18 inches in diameter must be replaced on the basis of one replacement tree for every one tree removed.

-	Individual trees of at least 18 inches in diameter but less than 24 inches in diameter must be replaced on the basis of two replacement trees for every one tree removed.

-	Individual trees of 24 inches in diameter or larger shall be replaced on the basis of three replacement trees for every one tree removed.

Some trees may be removed without replacement trees being planted.  These are trees located in the area of the proposed building and within 15 feet of the foundation, parking areas, driveways and private streets.

Replacement trees should be of a species similar to the tree it is replacing.  Deciduous trees must be at least 2.5 inches in caliper.  Evergreen trees must be at least 6 feet in height.

Trees designated for removal within the limits of disturbance may be transplanted within the site and counted as replacement trees.

SECURITY AGREEMENT

The City may require a performance bond, letter of credit or cash escrow deposit equal to 125 per cent of the value of the replacement trees.

TREE PRESERVATION ORDINANCE

This handout is a summary of the regulations found in Saint Paul’s Tree Preservation Ordinance.  The full text of the Tree Preservation Ordinance can be found in Chapter 67.200 of Saint Paul’s Legislative Code.  Copies are available on-line at www.stpaul.gov/code (click on the link for chapter 67).

This information is also available on-line.  Go to www.stpaul.gov/dsi and click on “Zoning.”

Please call 651-266-9086 if you have any questions.    H:\COMMON\ZONE\Site plan handouts\Tree pres.wpd              November 13, 2008